I. GENERAL:

Scope of Work - Furnish all necessary materials for the complete installation of aluminum hinged glass doors for this project as shown on the drawings and herein specified.  Doors shall be the "Series 1421F" as manufactured by Thermal Windows, Inc., Tulsa, Oklahoma.  The "Series 1421F" is a dual vent Hinged Glass Door with thermally improved main frame and vent consisting of side hinges, locking handle and multipoint lock system. The astrigal is attached to the secondary panel and the handle is attached to the primary panel only. The specifications and materials for the "Series 1421F" are as follows:

II. PRODUCTS:

Materials - Aluminum shall be of proper alloy for commercial window construction.  All extruded sections shall be of 6063-T5 aluminum alloy.

Frame - Main frame and sash members shall be a .062" nominal thickness.  Main frame shall be 3.250" in depth.  Horizontal and vertical vent members shall be hollow extrusions.  Main frames and vent members are to be extruded aluminum with a dual insulbar thermal barrier system creating a .625” wide thermal barrier.

Sill – Threshold for the 1421F is a .500” tall thermally broken aluminum extrusion with an EPDM  weatherseal. Check codes for FHA compliance. See drawing cuts.

Hardware – Operating handle shall be lever type connecting to a multi-point lock system. Handle is locked by a key cylinder from the outside with a thumb turn on the inside. Lock system engagements shall be as follows, Primary panel: Two (2) at handle, one (1) 2.500” from each end of lock stile and one (1) centered between handle and upper locking point. Secondary panel: Two (2) slide bolts are mounted to the astrigal and each engage a striker mounted at the head and sill. Slide bolts are operated individually. Door shall also be fitted with one (1) field adjustable limit device per panel at head to restrict door panel travel. Limit device shall also utilize a friction adjusting screw.

Hinges – Shall consist of four (4) extruded aluminum butt type hinges.  Hinge pins shall be .250” diameter stainless steel with hard vinyl bushings.

Weatherstripping – Door panel shall close to a full perimeter EPDM weatherseal utilizing welded corner construction.

III. CONSTRUCTION:

Assembly – Main frame and door panel corners shall be

of mitered, sealed, crimped and staked corner construction. Each corner shall consist of one extruded aluminum corner key held in place with two die cast retainer pins, one die cast corner key staked in place and one friction fit hard vinyl corner key. Threshold is mechanically fastened and sealed between the jambs.

Glazing - Glass in the door panel shall be factory glazed using EPDM gasket at exterior perimeter with extruded aluminum glazing bead and EPDM wedge at interior of glass.  The insulated glass units shall be 1.000" overall thickness with two lites .125” Tempered glass, separated by a .750" air space for optimum insulation.  All insulated glass units shall meet the requirements of the ASTM E 2188-02 / ASTM E 2190-02 specification, Class "A".

Finish - Shall be a factory applied baked polyurethane powder coat finish meeting the requirements of AAMA 2604 for Pigmented Organic Coating on Extruded Aluminum.  Standard Tier I colors available are bronze, white, crème, sandstone, and almond.  Bronze anodizing, clear anodizing and high performance AAMA 605.2 finishes are optional.

Operation - The door panel is operable to the outside and lockable by key from the outside and thumb turn from the inside. Astrigal is mounted to secondary panel and is held in the closed position by manually operated slide bolts.

IV. PERFORMANCE:

Structural Performance, Air and Water Infiltration - Shall meet the requirements of ANSI/AAMA 101/I.S.2-97 HGD C-40 plus.

V. INSTALLATION:

Qualifications - Only skilled mechanics with experience in this trade.  Units shall be installed plumb, level, square and shall be secured in accordance with detailed shop drawings.  A non-hardening sealant compatible with aluminum shall be provided by the installer and applied in sufficient quantity to provide a weathertight seal between the window and surrounding construction.

Installation Details - The door manufacturer shall submit complete installation details for the Architects approval.  The drawings shall show elevations of windows, full size details of frame and vents, details of construction and anchorage of window.